## Slide 1
Verdi Area Multimodal Transportation Study
March 20, 2023

## Slide 2
Study Purpose
Conduct multi-modal analysis to identify:
  Corridor gaps in connectivity (vehicular, ped, bike, transit)
  Crash and congestion hot spots
Design a strategy for developing regional road transportation improvements
Identify short- and long-term improvements
Solicit feedback from and inform agencies, stakeholders, and general public throughout the process
Development permitting/requirements handled by respective local agency
Planning
Existing conditions/ needs assessment
Community visioning
Evaluation of alternatives
Action plan/ recommended improvements
Environmental
Environmental study (state or NEPA process)
Preliminary engineering
Agency issues decision
Design
Detailed corridor design
Right-of-way, utilities, and other impacts
Construction plans, permits, and funding secured
Construction
Build and deliver
WE ARE HERE
Notes: Add develop vision (is it a freeway, arterial or blend?)

## Slide 3
Study Limits

## Slide 4
Review existing conditions 
Identify gaps and needs 
Provide proposed project recommendations 
Primary focus on regional roads
Stakeholder outreach
Goals and Objectives

## Slide 5
Significant new development
Crashes primarily on I-80 (86% of overall crashes)
Traffic growth more significant at interchanges
Limited truck parking with spillover along 3rd Street and Verdi Road
Lack of pedestrian connectivity
Opportunity to enhance recreational bicycle access
OHV concerns and confusion on regulations/ordinances
Existing Conditions Summary

## Slide 6
Center for Advanced Transportation Education and Research (CATER)
Connected Vehicle Data
Sampling
  Weekday - March 9th – 11th
  Weekend – March 13th & 14th
UNR Speed Study
Route | Posted | Weekday | Weekend | Data Sets
US 40 East | 45 mph | 37 mph | 38 mph | 210
US 40 West | 45 mph | 37 mph | 39 mph | 74
I-80 East | 65 mph | 70 mph | 70 mph | 308
I-80 West | 65 mph | 70 mph | 70 mph | 474
Bridge St | 25 mph | 15 mph | 18 mph | 43
S. Verdi Rd | 25 mph | 28 mph | 28 mph | 23
Average Speed

## Slide 7
Coffee with the RTC Study Team – June 10, 2022
  On-site tablets with survey
  Fact sheets
Areas of Concern
  Vehicular Speeds
  Verdi Road
  Bus Service
  More Walkable/Bikeable
  Better Freeway Access
  Intersection Safety
  Wildlife Concerns
  No More Development
  Leave Verdi Alone
Public Outreach and Feedback

## Slide 8
Near Term (NDOT Contract 3947 – Begin Spring 2023)
Wildlife Fencing 
Removal of I-80 Rumble Strips 
Mid Term
Median Cable/Barrier Rail Installation
Bridge Improvements (IIJA Funding)
Widen I-80/Truckee Bridges (IIJA Funding)
Long Term
Widen I-80 to Three Lanes
Reconfigure/Reconstruct Gold Ranch Interchange and Bridge
Proposed Area Improvements - Interstate 80

## Slide 9
Proposed Area Improvements - Interstate 80
3rd Street
Gold Ranch Interchange



P-n-R
Garson Road Interchange
Garson Road
Preliminary Subject to Change

## Slide 10
Vehicular
Verdi Road
  Paved width 22’ and 2’ – 4’ gravel shoulders
  Steep slopes each side (cut-south, fill-north)
  Community concerns of cars going down slope
  Portion within UPRR right-of-way
  420 AADT (2021)
  Poor cost/benefit & prioritization
Option 1 - $$$$
  Two-way roadway – 11’ lanes and 2’ shoulders
  Provide guardrail on north side
  Significant retaining wall work on south side
    5’-8’ tall
Option 2 - $
  Convert to one-way
  Provide guardrail
  10’ travel lane, 8’ shared use path
Either option may require upgrades to UPRR/Bridge Street signal crossing
Proposed Area Improvements – Regional Roads

## Slide 11
Pedestrians and Bicyclists
Enhance Edinburgh roundabout
  Provide bicycle ramps to utilize crosswalks
Shared Use Paths
  3rd Street
  Bridge Avenue
    3rd Street to Verdi Elementary
    3rd Street to Verdi Road (UPRR Crossing)
  Bridges
    Truckee 3rd Street (east)
    Truckee 3rd Street (west)
    Canal 3rd Street
  Crystal Peak Drive under I-80
Proposed Area Improvements – Regional Roads

## Slide 12
Freight
  Freight plan to continue addressing truck parking and advance notification of I-80 closures
  Private parcels near Gold Ranch and Mogul & 4th Street
  RTC regional freight study (upcoming)
Park-n-Rides
  New Gold Ranch interchange
  Partnership with Boomtown Casino
Transit
  Focused educational outreach to Verdi area
Speed Management
  Reduce lanes to 11’ on 3rd Street (US 40) from Exit 2 to Exit 5
  Continue working with law enforcement
Proposed Area Improvements – Additional

## Slide 13
Proposed Area Improvements - Summary

## Slide 14
Adjust recommendations based on CAB/NAB feedback
Prepare draft report
Solicit public feedback
Agency review
Address comments and submit final report
Next Steps

## Slide 15
THANK YOU
Regional Transportation Commission of Washoe County
In association with
CA Group and Parametrix
Truckee Meadows/Verdi
Citizen’s Advisory Board Meeting
xwang@rtcwashoe.com
chad.anson@c-agroup.com
Building A Better Community Through Quality Transportation
rtcwashoe.com